## Slide 1: A SAT-Based Routing Algorithm for Cross-Referencing Biochips
Ping-Hung Yuh1, Cliff Chiung-Yu Lin2, Tsung-Wei Huang3, Tsung-Yi Ho3, Chia-Lin Yang4, and Yao-Wen Chang5
1TSMC 2EE, Stanford 3CSIE, National Cheng Kung University 4CSIE, National Taiwan University 5GIEE & EE, National Taiwan University

## Slide 2: Outline
Introduction
Droplet Routing on Cross-Referencing Biochips
Experimental Result
Conclusion

## Slide 3: Outline
Introduction
Droplet Routing on Cross-Referencing Biochips
Experimental Result
Conclusion

## Slide 4: Digital Microfluidic Biochips
Perform laboratory procedures based on droplets
  Droplet: biological sample carrier
Three main components:
  2D microfluidic array: set of basic cells for biological reactions
  Reservoirs/dispensing ports: for droplet generation
  Optical detectors: detection of reaction result
The schematic view of a biochip (Duke Univ.)
Reservoirs/Dispensing ports
Optical detector
Droplets
Electrodes
Mixing two droplets
2D microfluidic array
Notes: Digital microfluidic biochips are used to perform laboratory procesudes based on droplets, where droplets are biological sample carriers.
This figure shows the schematic view of a digital microfluidic biochip developed by the Duke University.
There are three main components
The first one is the 2D array that is used for reaction.
The second one is the reservoirs/dispensing ports that are used for droplet generation.
The third one is the optical detectors that are used for the detection of reaction result.

## Slide 5: Biochip Architectures
Direct-addressing biochips
  Each cell is individually controlled
  # of control wires (for cell activation) is proportional to the area of a biochip
  Only suitable for small-scale biochips
Cross-referencing biochips [Gong et al, MEM’04]
  A control pin is used for a row/column of cells
  # of control wires is proportional to the perimeter of a biochip
  More suitable for large-scale biochips
Direct-addressing biochip
Cross-referencing biochip
Control wire

## Slide 6: Bioassay Execution and Droplet Routing
Bioassay: a procedure to determine the strength or activity of a biological sample
Droplet routing
  Droplet transportation from its source pin to target pin
  2-pin & 3-pin nets
  Set of 2D planes
Task graph
Bioassay execution illustration
a
Mix
Dilution
c
b
Generation
d
e
c
a
Droplet routing path
e
Mixing point
d
d
Routing obstacle
Pin

## Slide 7: Droplet Movement and Electrode Interference
Cell activation: a potential difference on this cell
Electrode interference: extra-activated cells to prevent correct droplet movement
  Due to voltage assignment on rows/columns
High voltage
3
Low voltage
Activated cell
Extra activated cell
1
2

## Slide 8: Routing Constraints
Electrode constraint
  Avoidance of electrode interference
  Only one neighboring cell can be activated for correct droplet movement
Fluidic constraint
  For the correctness of droplet transportation
  3D cube in a 3D space
Electrode constraint
Deactivated cell
Activated cell
(x, y, t)
(x-1, y-1, t-1)
(x+1, y+1, t+1)
Fluidic constraint

## Slide 9: Problem Formulation
Given:
  A set of 2-pin or 3-pin nets; location of pins and obstacles
Objective:
  Voltage assignment for correct droplet movement
  Minimize maximum droplet transportation time for fast bioassay execution
Constraints:
  Both the electrode and static fluidic constraints are satisfied
Routing problem
Droplet routing

## Slide 10: Previous Work
Routing algorithms for direct-addressing biochips
  [Su et al, DATE’06], [Griffith et al, TCAD’06], [K. Böhringer, TCAD’06], [Yuh et al, ICCAD’07], and [Cho et al, ISPD’08]
Indirect method
  A direct-addressing routing solution must be given
  Graph coloring based approach [Griffith et al, TCAD’06]
    # of colors = # of cycles to move all droplets
  Clique partitioning based approach [Xu et al, DATE’07]
    # of cliques = # of cycles to move all droplets
Direct method
  ILP-based routing [Yuh et al, DAC’08]

## Slide 11: Our Contribution
Propose the first SAT-based routing algorithm
  More efficient than generic ILP formulation
Two-stage routing algorithm
  Global routing followed by detailed routing
  Routing path information utilization
3D routing graph for detailed routing
  2D routing graph implies that a droplet can visit one basic cell at most once
  Higher flexibility

## Slide 12: Outline
Introduction
Droplet Routing on Cross-Referencing Biochips
  Algorithm Overview
  Global routing
  Detailed routing
Experimental Result
Conclusion

## Slide 13: Routing Algorithm Overview
Net criticality determination
Nets selection
SAT formulation construction
Nets routing
All nets are routed?
Inputs: 1. Net list 3. obstacle 2. pin locations locations
Global routing
3D routing and voltage assignment
Failed nets re-route
Refinement
Success?
No
Yes
No
Yes
Detailed routing

## Slide 14: Outline
Introduction
Droplet Routing on Cross-Referencing Biochips
  Algorithm Overview
  Global routing
  Detailed routing
Experimental Result
Conclusion

## Slide 15: Net Selection
Iteratively select nets whose criticality value is the largest one in global routing stage
Interference value of a net = possibility of violating fluidic + possibility of violating electrode constraints
Criticality = sum of interference values of all other nets
Less possible for fluidic constraint violation
Possible routing path
Less possible for electrode constraint violation

## Slide 16: Objective Function
Divide the entire cells into several 3 X 3 global cells (G-cell)
  Reduce the design complexity
  Avoid fluidic constraint violation
Minimize routing time and routing congestion
  Routing time is for fast droplet transportation time
  Congestion minimization is for electrode constraint
  A droplet introduces one unit of congestion for a “cross” of global cells
(0,0)
(0,2)
(0,3)
(3,0)
(1,3)
(1,1)
(1,0)
(0,1)
(2,3)
(2,2)
(2,1)
(2,0)
(3,3)
(3,2)
(3,1)

## Slide 17: Constraints
Objective function computation
  For droplet arrival time and congestion of global cells
Source/sink requirement
  All droplets are located at their source at time zero
  A droplet stays at its sink once reaching it
Exclusivity constraint
  Each global cell has one droplet at a time
Droplet movement
  A droplet moves one neighboring cells or stall

## Slide 18: Outline
Introduction
Droplet Routing on Cross-Referencing Biochips
  Algorithm Overview
  Global routing
  Detailed Routing
Experimental Result
Conclusion

## Slide 19: Routing Graph Construction
3D routing graph
  A node represents a basic cell (x, y) at time t
  An edge represents that a droplet can move from one basic cell to another from time t to t+1
Advantages
  Model the droplet movements in 3D manner
  Higher flexibility than 2D routing graph
 | (x3, y3) | 
(x5, y5) | (x, y) | (x1, y1)
 | (x4, y4) | 
(x, y, t)
(x2, y2, t+1)
(x4, y4, t+1)
(x1, y1, t+1)
(x3, y3, t+1)
(x, y, t+1)

## Slide 20: Routing Node Cost
Cost(x, y, t) = timing cost + fluidic penalty + electrode penalty + activation penalty + deactivation penalty
  Timing cost = a constant for non-sink nodes
  Fluidic penalty = # of fluidic constraint violated if this node is used for routing
  Electrode penalty = # of activated cells so that using (x, y) will violate electrode constraint
  Activation penalty = # of electrode constraint violation if (x, y) is activated
  Deactivation penalty = # of deactivated cells so that proper droplet routing is not possible

## Slide 21: Routing Algorithm
Iteratively route each net based on its criticality
Voltage assignment of each cell of the routing path
Terminate when all droplets reach their sinks or a limited iteration count is reached
A post-refinement is performed for further optimization

## Slide 22: Outline
Introduction
Droplet Routing on Cross-Referencing Biochips
Experimental Result
Conclusion

## Slide 23: Experimental Settings
Implemented our algorithm in C++ language on a 2.6 GHz Linux machine with 6GB memory
  SAT solver: minisat+
Compared with two indirect algorithms ([Griffith, et al, TCAD’06] and [Xu et al, DATE’07]) and one direct algorithm ([Yuh et al, DAC’08])
  Use BioRoute ([Yuh et al, ICCAD’07]) to generate direct-addressing routing solutions

## Slide 24: Routing Benchmark
Two real bioassays
  In-vitro diagnostics ([Su et al, DATE’06] & [Yuh et al, ICCAD’07])
  Protein analysis ([Yuh et al, ICCAD’07])
Bioassay | Chip dim. | #2D planes | #Tnets
Diagnostic_1 | 16 x 16 | 11 | 28
Diagnostic_2 | 14 x 14 | 15 | 35
Protein_1 | 21 x 21 | 64 | 181
Protein_2 | 13 x 13 | 78 | 178
#2D planes: total # of 2D planes #Tnets: total # of nets

## Slide 25: Routing Result
Report max/avg routing time and CPU time
Better solution quality within reasonable CPU time
Circuit | Xu et al, DATE’07 |  | Griffith, et al, TCAD’06 |  | Yuh et al, DAC’08 |  | Ours | 
 | Time (clk) | CPU time (sec) | Time (clk) | CPU time (sec) | Time (clk) | CPU time (sec) | Time (clk) | CPU time (sec)
Diag_1 | 40/ 16.72 | < 0.01 | 47/ 20.18 | 0.01 | 24/ 13.09 | 0.54 | 19/ 12.36 | 2.66
Diag_2 | 35/ 13.46 | < 0.01 | 52/ 16.80 | 0.01 | 21/ 10.93 | 0.57 | 20/ 10.20 | 2.64
Pro._1 | 48/ 10.32 | < 0.01 | 55/ 24.40 | 0.05 | 25/ 16.15 | 3.40 | 23/ 15.78 | 9.84
Pro._2 | 36/ 11.00 | < 0.01 | 53/ 14.33 | 0.03 | 29/ 10.47 | 1.43 | 21/ 9.25 | 6.97

## Slide 26: Routing Result of Diagnostic_1
obstacle
High voltage
Low voltage

## Slide 27: Outline
Introduction
Droplet Routing on Cross-Referencing Biochips
Experimental Result
Conclusion

## Slide 28: Conclusion
Proposed the first SAT-based droplet routing algorithm for cross-referencing biochips
Proposed the two-stage routing scheme
  Global followed by detailed routing
  Routing information utilization
Demonstrated the effectiveness of our approach
Future work
  Other routing objectives, such as power minimization